==================================================================
   DOS / PC / RSS Information                  For Motorola RSS Users

   DOS_INFO.DOC   15jun97                  Copyright(c) Motorola Inc.
   Radio Software Technology Center        LMPS, Ft. Lauderdale,  FLA
   ==================================================================

   This information is intended to aid our RSS Users in understanding
   how the PC, DOS and the RSS work together to program and service
   Motorola Radio Products.  No representation is made that this
   information is complete or accurate.  Motorola expressly disclaims
   any liability for the accuracy or completeness of the information, or
   for any damages resulting from the use or misuse of the information.

   Please refer to the manufacturer's documents for your particular
   system.  Additional information on the use of PCs and DOS can be
   found in commonly-available DOS/PC references.  Later versions of
   DOS (5.x and 6.x) include the "HELP [command]" command.

   Copyrights, Trademarks, and Service Marks for various companies and
   products mentioned below are the sole property of the manufacturers,
   and are hereby acknowledged as such.


   ==================================================================
   This file contains the following topics:

   (1)     DOS / PC (Troubleshooting) Setup Checklist
   (2)     Multiple DOS Configurations
               (Multiple CONFIG.SYS / AUTOEXEC.BAT files)
   (3)     Attempting to Execute RSS Under WINDOWS
   (4)     CAUTIONS When Using FLOPPY DISKETTES for Archiving Codeplugs
   (5)     "Sorting" Codeplug-File Directory Entries, for Faster Finding
   (6)     DOS Extended Error Codes
   ==================================================================



   ==================================================================
   ==================================================================
   SECTION (1)

   DOS / PC (Troubleshooting) Setup Checklist
   ==================================================================

   If you are having difficulty running RSS products on newer PCs -or-
   Laptop PCs, especially older versions of the RSS products, the tips
   below may help you.  We strongly suggest trying these items
   -PRIOR- to calling Motorola Customer Service for aid.

   Because PCs and DOS are rapidly changing and expanding their
   architectures, it may not be possible for older RSS versions to
   successfully run on the latest machines.  If these tips don't work
   for your old versions, we suggest contacting Motorola Americas Parts
   Division for an RSS upgrade.  If you have the latest version and
   still have problems after trying these tips, please contact Motorola
   Customer Service.

   The items below are suggested as a starting place.  You must consult
   your manufacturer's manuals for details on how to access your CMOS
   setup, and other PC-specific operations.  Your DOS manual must be
   consulted for DOS version-specific information.  Also, consult the
   README.TXT file on the RSS installation disk for the most current RSS
   information.

   -------------------------------------------------
   (-A-)   VERIFY RIB, CABLES and SETUP are OK:
   -------------------------------------------------
   Using your older PC, verify that the RIB, CABLE and Radio setup is
   working correctly.  After this step, move the PC-to-RIB cable from
   your original PC to you new PC's Comm. Port, remembering that the
   Comm. Port number (COM1 or COM2) may be different. See RSS Manual for
   Comm. Port selection and the "COMMUNICATIONS TEST" function.

   If no older PC is available, try changing the RIB, CABLES and Radio
   to verify proper hardware operation; also, ensure proper Comm. Port
   selection.

   ----------------------------
   (-B-)  MEMORY CONFIGURATION:
   ----------------------------
   Modern PCs and DOS can support four types of memory;

       (1) CONVENTIONAL - The lowest 640 KB of memory address space. This
       is the primary memory of all PCs.  Those RSS products that do
       -not- use EXTENDED memory need as much of this space as possible.

       (2) UPPER - The next-highest 384 KB memory address space.
       Application programs normally do not access this memory.  This space
       contains VIDEO/DISPLAY and other device data.  It also can be used to
       load certain device drivers "HIGH", to free-up some CONVENTIONAL
       memory.  !! CAUTION !! Some driver programs do not run in the UPPER
       memory area. On 80386 (and above) PCs, access to UPPER memory requires
       use of the EMM386.EXE memory manager.

       (3) EXTENDED/HIGH - Together, CONVENTIONAL and UPPER memory take up
       the first 1 MB of memory.  EXTENDED memory is all memory above the
       1 MB address.  The HIGH memory area is actually the first 64KB of
       EXTENDED memory space.  Loading DOS "HIGH" puts most of DOS in this
       HIGH area.  On 80286 (and above) PCs, the EXTENDED/HIGH memory can be
       accessed using an extended memory manager such as HIMEM.SYS.  Many
       RSS products require EXTENDED memory.

       (4) EXPANDED - This type of memory is not directly accessable to
       programs.  It normally was installed using an expanded-memory board,
       and required an expanded-memory manager to "map" the physical memory
       into the program's address space.  Today, EXPANDED memory can be
       "emulated" by managers such as EMM386.EXE, which use EXTENDED memory
       to emulate the expanded-memory card.  EMM386.EXE can also be used
       to load certain device drivers "HIGH", into the UPPER memory.

   Memory management begins with statements placed in the CONFIG.SYS
   and AUTOEXEC.BAT files.  Memory configuration should ideally
   maximize the amount of CONVENTIONAL and EXTENDED memory available, by
   using HIMEM.SYS and loading "DOS=HIGH" (in CONFIG.SYS).

   To repeat for clarity, loading DOS "HIGH" actually puts DOS into the
   HIGH portion of EXTENDED memory.  Loading device drivers "HIGH" puts
   them into the UPPER memory area (requires EMM386.EXE).  Both techniques
   can be used to free-up CONVENTIONAL memory, if needed.

   !! NOTE !! The DOS 5.x/6.x command "MEM /C | MORE" can be used to profile
   your memory configuration, and monitor changes in memory allocation when
   CONFIG.SYS and AUTOEXEC.BAT are changed.

   RSS products do -NOT- require EXPANDED memory, and if EMM386.EXE is
   used for either EXPANDED -or- UPPER memory access, enough EXTENDED
   memory must be left free for RSS allocation.  Consult the RSS User's
   Guide or the README.TXT file on the RSS installation disk to
   determine how much EXTENDED memory is required.

   Additional CONVENTIONAL memory can be freed by using EMM386.EXE to
   load selected device drivers into the UPPER area, using the "ram 64"
   switch (see DOS "HELP EMM386.EXE").  The "noems" switch can prevent
   some RSS products from executing properly on some machines, under
   some DOS versions.

   ----------------------------
   (-C-)   CONFIG.SYS
   ----------------------------
   As part of your troubleshooting, remember that DOS does -NOT- require
   CONFIG.SYS and AUTOEXEC.BAT to be present at startup.  When these two
   files are absent, this gives you a "clean start" (e.g. -NO-
   conflicting drivers, and -NO- "Terminate, Stay Memory Resident" (TSR)
   programs). Any RSS -not- requiring EXTENDED memory should be able to
   run with -no- CONFIG.SYS / AUTOEXEC.BAT.

   !! CAUTION !! There are some PC "security" programs that don't allow
   the CONFIG.SYS and/or AUTOEXEC.BAT files to be missing or altered.
   Check with your PC System Administrator if this is the case.

   !! CAUTION !! For ultimate safety, create a "bootable" floppy
   diskette, using the DOS "FORMAT /S" command, and copy your original
   CONFIG.SYS / AUTOEXEC.BAT files to the formatted floppy diskette.

   Do NOT delete your original CONFIG.SYS and AUTOEXEC.BAT files; instead,
   rename them (DOS "REN" command) to CONFIG.001 and AUTOEXEC.001.  Then,
   later, you can "COPY" them back to the standard names, and edit them
   for changes.

   For PCs with EXTENDED memory, the following -minimal- CONFIG.SYS
   should work for -all- RSS products, and HIMEM.SYS is REQUIRED for RSS
   products that need EXTENDED memory;

       DEVICE=C:\DOS\HIMEM.SYS /V
       DOS=HIGH
       BUFFERS=20
       FILES=20
       STACKS=9,512
       ( Device=C:\DOS\.... no entries at start of troubleshooting )

   !! CAUTION !! It is (Microsoft) recommended practice to always load
   HIMEM.SYS as the  -1st-  line of the CONFIG.SYS;   -IF-   EMM386.EXE
   is used, it should be the  -2nd-  line, with "DOS=HIGH,UMB" as the
   -3rd-  line.  ALWAYS put the "memory manager" entries -prior- to the
   "memory user" entries.  Reversing them may appear to work, but is not
   a stable configuration.  HIMEM should be -prior- to EMM386.

   For maximum availability of CONVENTIONAL memory, EMM386.EXE can be used
   to load device drivers "HIGH" into Upper Memory Blocks:

       DEVICE=C:\DOS\HIMEM.SYS /V
       DEVICE=C:\DOS\EMM386.EXE RAM 64
       DOS=HIGH,UMB
       BUFFERS=20
       FILES=20
       STACKS=9,512
       ( DeviceHIGH=C:\DOS\.... no entries at start of troubleshooting )

   If you are able to find the simplest CONFIG.SYS (with -NO- AUTOEXEC.BAT)
   that enables RSS execution, then lines from the original CONFIG.SYS can
   be restored one at a time to resolve which element is in conflict with
   the RSS execution. Use DOS 5.x/6.x "MEM /C | MORE" to view memory area
   allocation, as you make changes.

   Once a stable CONFIG.SYS is established, begin building back the
   AUTOEXEC.BAT, starting with the "SET PATH=C:\DOS;C:\....." line.

   Some drivers/utilities to watch for in CONFIG.SYS and AUTOEXEC.BAT;

       1)  The DOS "SHARE" Program causes problems with some RSS products.
       2)  The DOS "GRAPHICS" Program causes problems with some RSS products.
       3)  The DOS "EMM386" Expanded Memory Mgr. "noems" switch can conflict
           with some RSS products.
       4)  The DOS "POWER.EXE Program can interfere with some LapTop power
           management systems (see below).

   ----------------------------
   (-D-)   CMOS SETUP
   ----------------------------
   Most modern PCs have CPU speed selection and "caching" options as
   part of their CMOS setup.  To begin your troubleshooting, set CPU to
   the lowest possible speed, and turn -all- cache (internal and
   external) off.  Both the high speed and caching can interfere with
   timing when reading/writing the Radio through the RIB box.

   ----------------------------
   (-E-)   POWER MANAGEMENT
   ----------------------------
   LAPTOPS (and some newer desktops as well) have power management
   features to conserve operating power. The interrupt used in this
   process cannot be turned off by applications, and typically takes a
   -long- time to service the various devices, and this can interfere
   with timing when reading/writing the Radio through the RIB box.  Turn
   the power management OFF, or to the least-active mode allowed.

   There are some PC manufacturers who are advising that the Microsoft
   POWER.EXE driver be REMOVED from the CONFIG.SYS file, because it may
   interfere with the PC's internal power management functions.  Consult
   your manufacturer's literature.

   In some cases, power management must be disabled at several different
   levels; the PC's CMOS setup, the CONFIG.SYS/AUTOEXEC.BAT files, and
   the Windows environemnt.

   -------------------------------------------------
   (-F-)  8250/16450/16550 Communications Port UARTs
   -------------------------------------------------
   The 16550 UART (Universal Async. Receive/Transmit) is functionally
   equivalent to the 8250 and 16450 UARTs, with the addition of 16-byte
   XMIT/RECV FIFO buffers.  To conserve power and chip count, many
   manufacturers are using custom-ICs to -emulate- the 16550 UART.  Some
   emulations are variants, such as powering up with the FIFO enabled (a
   true 16550 powers up with FIFO -disabled-).

   The symptom would be repeated errors while trying to READ/WRITE the
   Radio Codeplug via the RIB box.  This is most likely to be seen on
   LAPTOP PCs, but can occur on some DESKTOPs as well.

   Some manufacturers are supplying a utility program that allows the
   user to -disable- the FIFOs, for backwards compatibility.  For
   example, COMPAQ supplies "COMFIFO.EXE" (c) for their "Contura Aero (c)"
   Laptop series.  Consult your manufacturer's literature and/or THEIR
   Customer Service.

   Motorola LMPS Product Services can supply a utility called COMMCHEK.EXE
   which can report/change the FIFO state if the UART(s) are 16550 or
   compatible.


   ==================================================================
   ==================================================================
   SECTION (2)

   Multiple DOS Configurations (Multiple CONFIG.SYS / AUTOEXEC.BAT files)
   ==================================================================

   It may be that you will need to keep more than one set of CONFIG.SYS and
   AUTOEXEC.BAT files, switching to one set for a specific applications'
   use, then switching to another set for use with RSS programs. A sample
   "batch" file, SWITCH.BAT, is shown below, and can be used to quickly
   switch to a desired pair of CONFIG/AUTOEXEC files:

   e.g. '\SWITCH RSS' switches to the RSS pair of configuration files, then
   the PC is re-booted with CTL-ALT-DEL.

       @echo OFF
       echo   -SWITCH-    autoexec + config   to  %1
       if %1- == rss-  GOTO DO_RSS
       if %1- == act-  GOTO DO_ACT
       echo ERROR !!   arg1 value -NOT- equal to;
       echo   rss      Motorola Radio Service Software
       echo   act      For Accounting/Payroll Applications
       GOTO   END

       :DO_RSS
       copy   C:\autoexec.RSS   C:\*.bat
       copy   C:\config.RSS     C:\*.sys
       echo   READY FOR --RSS--
       GOTO   END

       :DO_ACT
       copy   C:\autoexec.ACT   C:\*.bat
       copy   C:\config.ACT     C:\*.sys
       echo   READY FOR --ACCOUNTING--
       GOTO   END

       rem    additional applications can be added....

       :END
       echo   READY FOR -- SYSTEM RE-BOOT --
       echo   END of -SWITCH-

   A more general (and cryptic) method is the following non-specific
   version which would accept any 3-letter file suffix, but requires
   that all users remember which file pair is for a specific
   application:

       @echo   off
       echo    SWITCH_2
       echo    Arg_1 = %1

       if %1- == - goto ERROR
       if NOT EXIST    autoexec.%1   goto ERROR_2
       if NOT EXIST    config.%1     goto ERROR_2
       goto DOIT

       :ERROR
       echo ERROR: NEEDS -3- letter suffix argument as Arg1
       goto END

       :ERROR_2
       echo ERROR: CANNOT find autoexec/config  - .%1 -
       goto END

       :DOIT
       echo    copy C:\autoexec.%1   c:\autoexec.BAT
       copy    C:\autoexec.%1   c:\autoexec.BAT
       echo    copy C:\config.%1     c:\config.SYS
       copy    C:\CONFIG.%1     c:\config.SYS

       :END
       echo    READY FOR -- SYSTEM RE-BOOT --
       echo    END of SWITCH_2

   Advanced Users may wish to consult DOS 6.xx "HELP MULTI-CONFIG" for
   information on using MENU commands within a single CONFIG.SYS and
   AUTOEXEC.BAT pair, which allows different DOS configurations by
   user's choice from a menu, at boot-up time.


       REM    WINDOWS 3.1 / DOS   MENU CONFIG.SYS

       [menu]
       menuitem=WIN_31, Windows-3.1
       menuitem=DOS,    MS-DOS 6.22
       menudefault=WIN_31

       [WIN_31]
       Device=C:\WINDOWS\HIMEM.SYS /V /TESTMEM:OFF
       Device=C:\WINDOWS\EMM386.EXE RAM 64

       [DOS]
       Device=C:\DOS\HIMEM.SYS /V /TESTMEM:OFF
       Device=C:\DOS\EMM386.EXE RAM 64

       [common]
       DOS=HIGH,UMB
       STACKS=9,512
       LASTDRIVE=E
       DeviceHIGH=C:\MOUSE\LMOUSE.COM

       --------------------------------------------

       @ECHO   OFF
       REM     Windows-3.1 -or- DOS 6.22 --- MENU AUTOEXEC.BAT

       prompt  $P$G
       SET     TEMP=C:\temp
       SET     TMP=C:\temp
       SET     COPYCMD=/Y

       rem CONFIG.SYS sets -menu- Value in DOS ENV. Var. "CONFIG"
       GOTO    %CONFIG%

       :WIN_31
       SET     PATH=C:\WINDOWS;C:\WINDOWS\SYSTEM;.;C:\dos;C:\utils;
       goto    END

       :DOS
       SET     PATH=.;C:\dos;C:\utils;
       goto    END

       :END
       DOSKEY


   ==================================================================
   ==================================================================
   SECTION (3)

   Attempting to Execute RSS Under WINDOWS    [*]=(tm) Microsoft Corp
   ==================================================================

   The original PC/DOS design is based on the assumptions of:
       1)  Single User.
       2)  Single Application/Task active at one time.
       3)  Direct access to hardware by Application software.

   Communications applications, such as the RSS, rely on these
   assumptions to give them the priority (no multi-user, multi-tasking
   interference) and speed (direct hardware access) to maintain the
   critical timing needed to sustain a communications protocol.

   Windows (and many networked environments) must assume:
       1)  Multiple Users possible (e.g. networking).
       2)  Multiple Tasks "Active" at same time. (multi-tasking)
       3)  Direct access to hardware by applications not allowed.

   We cannot guaruntee successful operation of any RSS under Microsoft
   Windows[*].  Windows will not allow programs direct access to the
   Comm. Port and Timer hardware; these functions are emulated by
   Windows, hence they are slower than under DOS, and this could
   interfere with critical communications timing.  Higher-speed CPUs/PCs
   (80486+ at 66 MHz and above) have the best chance of success.

   Any setup for RSS within Windows 3.1 [*] or Windows 95 [*] should be
   done in the DOS FULL-SCREEN Mode, as opposed to the DOS WINDOW Mode.
   Communications programs (i.e. RSS Reading / Writing the Radio
   Codeplug) cannot be executed successfully in WINDOW "background"
   mode, and the WINDOW "foreground" mode may not sufficiently support
   the critical timing needed to consistently communicate with the
   RIB/Radio. FULL-SCREEN Mode gives higher priority (speed) to the RSS
   than the DOS WINDOW Mode.

    For Windows 3.1, use the PIF EDITOR to open the DOSPRMPT.PIF file.
       Set "Display Usage" to FULL SCREEN and "Execution" to EXCLUSIVE.
       Under "ADVANCED", set "Foreground Priority" to 10,000, and set the
           "Detect Idle Time" box OFF.  SAVE the file before using the
           "MS-DOS PROMPT" icon.

    For Windows 95, create an icon/shortcut.  Under PROPERTIES:
       Select PROGRAM Sheet;
           set "CLOSE ON EXIT" box TRUE.
       Under "ADVANCED";
           set "PREVENT PROGRAM FROM DETECTING WINDOWS" to TRUE.
           set "SUGGEST MS-DOS MODE" to FALSE.
           set "MS-DOS MODE" to FALSE.
       Select SCREEN Sheet;
           set "USAGE" to FULL SCREEN.
       Select MISC Sheet;
           set "ALLOW SCREENSAVER" to FALSE.
           set "IDLE SENSITIVITY" to LOW.

   If the above does not allow the RSS to function properly, then;
       a) EXIT Windows 3.1 and use normal DOS.
       b) Set Windows 95 PROGRAM/ADVANCED Sheet to "MS-DOS Mode".


   ==================================================================
   ==================================================================
   SECTION (4)

   CAUTIONS When Using FLOPPY DISKETTES for Archiving Codeplugs
   ==================================================================

   If you are using FLOPPY DISKETTES for archiving your codeplug files,
   please keep the following in mind;

   A)  Due to ambiguities in the (extended) error codes returned to an
   RSS from DOS/BIOS (See "DOS Extended Error Codes" below), the RSS
   cannot always properly report the precise nature of an error while
   reading/writing disk files.

   One example is using an UN-FORMATTED Floppy Diskette.  The DOS error
   code returned is "31", "GENERAL FAILURE" (type unknown).  This type
   of failure usually is interpreted by the RSS as an "immediate exit"
   situation, because the error could be from other resources, such as
   your -fixed- disk, and continuing could jeapordize your system/data.

   B)  Due to (A) above, you should ensure that -all- your diskettes are NEW
   and PROPERLY FORMATTED prior to using them for codeplug archives.

   C)  Floppy diskettes and -drives- are exposed to DIRT and MOISTURE.  Keep
   your diskettes in their sleeves and away from contaminants. Clean your
   -drives- periodically with commercially-available cleaning kits.

   D)  You should check the condition of your floppy diskettes PERIODICALLY,
   by running DOS "CHKDSK (A: -or- B:)" or (DOS 6.x) "SCANDISK (A: -or- B:)".
   If these DOS programs detect problems, even if "corrected", we recommend
   copying that diskette to a NEWLY FORMATTED diskette before continuing,
   and using the NEW diskette for future archiving.

   If problems persist, the diskette may be defective, -or- your -drive-
   may need cleaning or repair.

   E)  Using a floppy diskette that is ALMOST FULL can cause problems,
   such as not leaving enough room for renamed backups (the old version
   stays and the new version is added), not enough room for the next RSS
   database entry (into the *.DBF file), etc.  After each RSS session,
   perform a DOS "DIR (A:  -or- B:)"; the last entry of the report tells
   how many bytes are "free" on the diskette.  We recommend leaving at
   least 10,000 bytes free at all times.

   F)  An alternative to floppy diskettes is re-organizing the archive
   system on your -FIXED- disk.  The RSS allows multiple CODEPLUG or
   ARCHIVE subdirectories, under unique names, such that each sub-dir. can
   be organized by model number, customer, department, etc.  Create the
   sub-dirs. via DOS "mkdir -name-" command.  Then access each sub-dir.
   from the RSS using the "(F2) Change Archive" on the GET or SAVE screen.

   This offers the advantages of greater speed in finding files and in
   reading / writing files, much quicker access to various archives
   without changing diskettes, and higher limits on how many files can
   be in a single archive.

   These archives need periodic BACKUP to floppy diskettes (or -tapes-).
   Make sure you save -all- files in the archive sub-dir., to include some
   RSS "database" files (*.DBF).  Large sets of archive files can be backed
   up to floppy diskettes via "compression" programs that create "*.zip"
   files.  !! CAUTION !! The first file you should save to a compressed
   backup diskette is the version-matching "uncompress/unzip" program file.


   ==================================================================
   ==================================================================
   SECTION (5)

   "Sorting" Codeplug-File Directory Entries, for Faster Finding
   ==================================================================

   Many RSS programs were not designed to "sort" the file entries in a
   codeplug archive into an "ascending" number order, by serial number.
   Quickly finding a particular serial number from 100+ entries can be a
   problem. There are utilities available that can sort directory entries
   into ascending number order, making it easier to find particular serial
   numbers.

   One such utility is Peter Norton's (c) "DS" (Directory Sort, Version
   4.50).  It will read directory entries, sort them by several
   different user-chosen orders, and re-write the directory entries
   permanently in the new order.

   Another method is the DOS Version 6.x "DEFRAG" command, similar to
   Peter Norton's (c) "SPEEDISK" (Version 5.0);  both offer an option to
   sort files into ascending order while de-fragmenting your disk files.

   All of the above (and others) can be used on both -fixed- and -floppy-
   disk archive directories.  Please read the appropriate documents carefully.

   !! CAUTION !! Always backup your disk(ette) -prior- to first use of
   these utilities.

   NOTE !! These utilities will -not- change the order of files
   displayed with any RSS that requires a *.DBF file in the Archive
   sub-directory.  E.g. MaxTrac Conventional RSS always requires that a
   file "MAXTRACM.DBF" be present in any sub-directory that contains
   "valid" archive files.  The order of files displayed is determined by
   the order in which the files were saved and entered into the *.DBF file.


   ==================================================================
   ==================================================================
   SECTION (6)

   DOS Extended Error Codes
   ==================================================================

   The RSS Program is an application program that must use the PC's DOS
   (Disk Operating System) and BIOS Interfaces for access to computer
   resources such as memory, disk drives, disk files, printers,
   communication ports (e.g.  COM1), etc.

   If the RSS performs an operation on a resource, and DOS/BIOS detects an
   error, DOS will return an error code to the RSS.  This will most
   often (but not always) be reported in the form;

       Error Code          - nn    Gives Specific Error Information
       Error Class         - xx    Gives General Situation Information
       Locus               - yy    Gives General Source (Device) of Error
       Recommended Action  - zz    Gives Recommended (Recovery) Action

   In some cases, only the Error Code is shown.

   To aid users in resolving problems with computer resources, the
   following list of DOS Error Codes is given.  These Codes are commonly
   documented elsewhere as "DOS Extended Error Codes", under INT 59(hex)
   "GET EXTENDED ERROR INFORMATION".  Also shown are the CLASS and LOCUS
   Codes.

   The ACTION Codes are not shown.  The RSS has limited options to take
   any system-level "recovery action" without jeapordizing your data or
   your system. Some Codes are ambiguous.  Each new version of DOS can
   expand the number of defined Error Codes and/or expand the current
   definitions.  Also, various VERSIONS of DOS/BIOS can return different
   Codes, depending on their implementation.  E.g., a common return for
   attempting access to an un-formatted floppy disk is (CODE-CLASS-LOCUS)
   31-13-2 "GENERAL FAILURE",  not the possible  11-9-2  or  26-11-2.

   No representation is made that this list is complete or accurate.  Further
   information on the codes and terms shown below can be found in
   commonly-available DOS references.  Using the three Codes together may
   help you to find/correct any resource problems you are having.

   The Codes are shown as DECIMAL values.

   DOS EXTENDED ERROR CODES:
   =========================
   001 -   Invalid Function Number
   002 -   File Not Found
   003 -   (Dir/File) Path Not Found
   004 -   No (File) Handles Available (Too Many Files Open)
   005 -   Access Denied (e.g. Attempt to Write a Read-Only File)
   006 -   Invalid (File) Handle
   007 -   Memory Control Blocks Destroyed
   008 -   Insufficient (Not Enough) Memory
   009 -   Invalid Memory Block Address
   010 -   Invalid Environment Block

   011 -   Invalid Format
   012 -   Invalid (File) Access Code
   013 -   Invalid Data
   014 -   (RESERVED)
   015 -   Invalid (Disk) Drive (Specification)
   016 -   Attempt To Remove Current Directory
   017 -   Not The Same Device
   018 -   No More Files
   019 -   Disk Is Write Protected
   020 -   Unknown Disk Unit ID

   021 -   (Disk) Drive Not Ready
   022 -   Unknown Disk Command
   023 -   CRC Error (Disk File Data Error)
   024 -   Bad Disk Request Structure Length
   025 -   (Disk) Seek Error
   026 -   Unknown Media Type (e.g. Non-DOS Disk)
   027 -   (Disk) Sector Not Found
   028 -   (Printer) Out Of Paper
   029 -   Write Fault/Error
   030 -   Read  Fault/Error

   031 -   General Failure (Exact Nature UNKNOWN)
   032 -   (File) Sharing Violation (e.g. DOS "SHARE")
   033 -   (File) Locking Violation
   034 -   Invalid Disk Change
   035 -   (File) FCB Unavailable
   036 -   Sharing Buffer Overflow
   037 -   (RESERVED)
   038 -   Unable To Complete (Disk) File Operation
   039 -   (RESERVED)
   :::
   049 -   (RESERVED)

   050 -   Network Request Not Supported
   051 -   Remote Computer Not Listening
   052 -   Duplicate Name On Network
   053 -   Network Name Not Found
   054 -   Network Busy
   055 -   Network Device No Longer Exists
   056 -   Net BIOS Command Limit Exceeded
   057 -   Network Adapter (Hardware) Error
   058 -   Incorrect Network Response
   059 -   Unexpected Network Error
   060 -   Incompatible Remote Adapter

   061 -   Print Queue Full
   062 -   Not Enough Space For Print File
   063 -   Print File Deleted
   064 -   Network Name Deleted
   065 -   Access Denied
   066 -   Network Device Type Incorrect
   067 -   Network Name Not Found
   068 -   Network Name Limit Exceeded
   069 -   Net BIOS Session Limit Exceeded
   070 -   (Sharing) Temporarily Paused

   071 -   Network Request Not Accepted
   072 -   Print or Disk Redirection Is Paused
   073 -   (RESERVED)
   :::
   079 -   (RESERVED)

   080 -   File Already Exists
   081 -   (RESERVED)
   082 -   Cannot Make Directory Entry
   083 -   Fail On INT 24 (Critical Error Interrupt)
   084 -   Too Many Redirections (Out Of Network Structures)
   085 -   Duplicate Redirection (Network Device Already Assigned)
   086 -   Invalid Password
   087 -   Invalid Parameter
   088 -   Network Data Fault
   089 -   Function Not Supported By Network
   090 -   Required System Component Not Installed

   DOS ERROR CLASS CODES:
   ======================
   01  -   Out Of Resource; No More Left Of Whatever You Asked For
   02  -   Temporary Situation (e.g. Locked File); Try Again Later
   03  -   Authorization (Access Rights - Permissions)
   04  -   Internal DOS Error (Not User/Application);     CAUTION, SERIOUS !!
   05  -   Hardware Failure (Whatever Resource You Are Accessing). SERIOUS !!
   06  -   System Software Failure; Other DOS Problems;   CAUTION, SERIOUS !!
   07  -   Application Program (Software) Error
   08  -   Item (Resource) Requested Not Found
   09  -   Bad (Disk) Format ( e.g. Non-DOS Disk )
   10  -   Item (e.g. File) Locked
   11  -   Bad Media (e.g. Disk Sees CRC Errors On File Read, File Corrupted)
   12  -   Already Exists
   13  -   Error Class Is UNKNOWN

   DOS LOCUS CODES:
   ================
   01  -   Locus is UNKNOWN
   02  -   Block  (Data Transfer) Device (e.g. Disk Drive/RAM Disk Emulator)
   03  -   Network Device/Resource/Operation
   04  -   Serial (Data Transfer) Device (e.g. Comm. Port (COM1), Printer)
   05  -   Memory Related